# ACORN TECHNICAL MANUAL

Visual Display Unit Interlace Board. 200.002

(Teletext  VDU 40 )

Introduction 	page 	1

Parts List. 	page 	2

Board Layout 	page	3

Applications 	page 	4

Circuit Diagram 	page	9 & 10

Application Programs 	page 	11

# Introduction

The Acorn Visual Display Unit Controller Board connects to the Standard Acorn Computer Bus and contains a memory mapped character storage R.A.M. which is transparently written to or read from by the C.P.U.

An MC 6845 programmable controller I.C. provides all the synchronisation signals to drive a 625 line 50 fields per second V.D.U. together with read addresses for the character R.A.M. Characters are then fed to an SAA5050 character generator IC which produces the necessary dot patterns to create the characters to refresh the V.D.U.

The SAA5050 produces Teletext standard characters and has Red. Green and Blue drive outputs giving coloured characters or graphics.

The R.G.B. and sync outputs may be used to drive a colour encoder and modulator for a U.H.F. Television; also provided is a 1 volt / 75 ohm composite sync and video output which can directly drive a Monochrome Monitor on which the different colours will appear as different scales of grey.

The V.D.U. controller PCB is supplied in kit form with a full set of I.C. sockets. It is easily assembled using a small soldering iron and useful hints on assembly may be found in the Acorn Micro-computer system 1 Technical Manual. The board operates from a single +5v supply from which it draws not more than 500 mA.

Also provided are listings for programs which set up the MC6845, display 25 instructions in hex on the V.D.U. {with double or treble byte instructions on a single line) and allow the drawing or graphics or characters on the V.D.U. These programs may be loaded and run using the Acorn system 1 Monitor. A new monitor R.O.M. will shortly be available for linking the V.D.U. and an ASC II keyboard to Acorns' 4K Fast BASIC.

## PARTS LIST FOR ACORN V.D.U. CONTROLLER

PCB 	Acorn Computers Ltd. pt no 200,002

IC 1 	74LS139 decoder and 16 pin socket

IC 2 	74LSO2 NOR gate and 14 pin socket

IC 3 	74LS13 schmitt trigger and 14 pin socket

IC 4 	MC6845 C.R.T. controller and 40 pin socket

IC 5,6 & 7 	74LS157 data selector and 16 pin sockets

IC 8 & 9 	2114-3 R.A.M. and 18 pin sockets

IC 10 	74LS174 hex flip-flop and 16 pin socket

IC 11 	INS 8208 buffer and 20 pin socket

IC 12 	74LS86 excl or gate and 14 pin socket

IC 13 	SAA5050 character generator and 28 pin socket

IC 14 	74LS00 NAND gate and 14 pin socket

Q 1 	BC107 transistor

D 1 	1N4148diode

R 1	1 K resistor

R 2 	2K7 resistor

R 3 	470 R preset potentiometer

R 4 	10K resistor

R 5 	4K7 resistor not supplied with kit

R 6 	22K resistor

R 7 	4K7 resistor

R 8 	10K resistor

R 9-12 	4 off 10K resistors

R 13 	4K7 resistor

R 14 	10K resistor

R 15 	470R resistor

R 16 	82R resistor

R 17 	18K resistor not supplied with kit

R 18 	10K resistor

R 19 	10K resistor not supplied with kit

R 20-22 	3 off 10K resistors

C 1 	10 or 15 (F electrolytic capacitor

C 2-7 	6 off 47 nF capacitors

C 8 	270pF capacitor

C 9	15OpF capacitor

NB For IC11 INS8208 is equivalent to DP8304

## Applications

To use this board in the Acorn system a low for block zero signal must be present on pin 31A of the Acorn bus. This is provided by connecting pin 8 of IC9 to pin 31A of the connector on the 6502 C.P.U. board. The 5 volt regulator and the electrolytic capacitor must bE: removed from the C.P.U .board and an external 5 volt supply at 3 amps is required on pin 1 A of all boards for a system using the C.P.U., V.D.U. interface, 8K memory board and cassette interface.

A 1volt at 75 ohm video monitor may be driven directly from connections 14 and 15 on the front of the board. Alternatively UHF modulator may be driven which connects to the aerial input of a domestic television set using the circuit shown the component values given suit the Astec UM 1233E36 modulator although other types should work satisfactorily.  IC3 on the VDU board forms a 6MHz dot clock which is adjusted using the preset resistor R3 to give characters of the right width on a steady picture after MC6845 has been initialised using the Applications programmes.

The 1024 byte character memory appears in block zero of the Acorn address map filling pages 04, 05 06 and 07. Two registers, which set up the 6845, are at addresses 0800 and 0801 and these repeat throughout page 08. The register at 0800 is a 5 bit write only register used to determine which of the data registers is accessed at 0801. The data registers, their addresses and their functions are tabulated here.

Register 	Function 	Program 	Type 	No of Bits Used

Address 		Unit

00 	Horizontal total 	char 	Write only 	8

01 	Horizontal displayed 		" 	 	"	“	8

02 	H Sync Position 		" 		" 	" 	8

03 	H Sync Width 		" 		" 	" 	4

04 	Vertical total 	char row 		" 	" 	7

05 	V total adjust 	scan line 		" 	" 	5

06 	Vertical displayed 	char row 		" 	" 	7

07 	V sync position 	char row 		" 	" 	7

08 	Interlace mode 		-		" 	" 	2

09 	Max scan line address 	scan line 		" 	" 	5

0A 	Cursor start 	scan line 		" 	" 	5 + 2

0B 	Cursor end 	scan line 		" 	" 	5

0C 	Start address H 		-		" 	" 	6

0D 	Start address L 		-		"	" 	8

0E 	Cursor H 		-	Read/Write 	6

0F 	Cursor L 		-	Read/Write 	8

10 	Light pen H 		-	Read only 	6

11 	Light pen L 		- 	Read only 	8

Using the programs provided all these registers are initialised for 625 line, 50 fields per second, non-interlaced operation with 25 rows each of 40 characters.

Hardware scrolling is used in the system which, with transparent access, gives a clean display and uses only a very small proportion of C.P.U's time. The character memory may be read from or written to at any time like any other piece of R.A.M.

The lightpen input to the board may be used after breaking the link to 0v and fitting a 4K7 resistor for R5. When the lightpen input goes high the contents of the character refresh address counter are strobed into registers 10 and 11 i.e. high byte and low byte. Thus the screen co-ordinates of the pen position may be determined.

The SAA 5050 character generator produces the following characters represented by the hex bytes shown .

20	space	30	0	40	@	50	P	60	-	70	p

21	!	31	1	41	A	51	Q	61	a	71	q

22	“	32	2	42	B	52	R	62	b	72	r

23	£	33	3	43	C	53	S	63	c	73	s

24	$	34	4	44	D	54	T	64	d	74	t

25	%	35	5	45	E	55	U	65	e	75	u

26	&	36	6	46	F	56	V	66	f	76	v

27	‘	37	7	47	G	57	W	67	g	77	w

28	(	38	8	48	H	58	X	68	h	78	x

29	)	39	9	49	I	59	Y	69	i	79	y

2A	*	3A	:	4A	J	5A	Z	6A	j	7A	z

2B	,	3B	;	4B	K	5B	(	6B	k	7B	¼

2C	+	3C	<	4C	L	5C	½	6C	l	7C	||

2D	_	3D	=	4D	M	5D	(	6D	m	7D	¾

2E	.	3E	>	4E	N	5E	(	6E	n	7E	(

2F	/	3F	?	4F	O	5F	#	6F	o	7F	delete

Note that there are a few exeptions to the usual ASCII, the most noticeable of which is at 23 where

£ replaces # which is moved from 23 to 5F.

Also available are the following teletext control characters with their hexadecimal codes shown:

01	Alpha	Red	11	Graphics	Red

02		“	Green	12		“	Green

03		“	Yellow	13		“	Yellow

04		“	Blue	14		“	Blue

05		“	Magenta	15		“	Magenta

06		“	Cyan	16		“	Cyan

07		“	White	17		“	White

08	Flash	18	Conceal Display

09	Steady	19	Contiguous Graphics

0A	End Box	1A	Separated Graphics

0B	Start Box

0C	Normal Height	1C	Black Background

0D	Double Height	1D	New Background

1E	Hold Graphics

1F	Release Graphics

These characters affect the characters displayed to the right of them on a line, and provide the following options:-

ALPHA (COLOUR) 	causes following characters on the line to be in the colour specified.

GRAPHICS (COLOUR) 	In Graphics mode each character space displayed is divided into 6 	cells. Each cell is illuminated, in the specified colour, if a

corresponding bit in the ASCII code stored at that location is set.

The bit assignments are:

b0  	b1

b2	b3

b4	b6

Bit 5 in the byte is always set for a graphics character, if bit 5 is clear

then the upper case, alphabet and characters (, ½, (, ( , # ,@ are

available in the same colour .

FLASH 	causes the following characters on the line to flash.

STEADY 	terminates the flash option on a line.

END BOX & START BOX 	Are options for using the circuit to super- impose text onto a normal

TV picture.

DOUBLE HEIGHT 	Must appear on two consecutive lines followed by the same

characters in which case the characters fill the two lines specified.

NORMAL HEIGHT 	Clears the double height option on a line.

CONCEAL DISPLAY	Switches off the character on a line these can only be revealed by

applying a signal to the character generator chip (or deleting the

CONCEAL character).

CONTIGUOUS GRAPHICS 	In this mode the graphics cells in a character are joined up.

SEPARATED GRAPHICS 	In this mode the graphics cells are separated by one character bit

width.

NEW BACKGROUND 	Sets the background to the colour of the last colour specifying

character .

BLACK BACKGROUND 	Resets the background colour to black.

HOLD GRAPHICS 	Causes the last graphics character to be dis- played when a control

character is entered.

RELEASE GRAPHICS 	Causes a space (Background colour) to be dis- played when a control

character is entered.

The character generator assumes an initial setting at the start of each line of: -

ALPHA WHITE, STEADY, END BOX, NORMAL HEIGHT.

CONTIGUOUS GRAPHICS, BLACK BACKGROUND, RELEASE GRAPHICS.

## Application Programs VDU Controller

The program listed below may be loaded using the Acorn system 1 monitor starting at address 0300. This program is intended to be used as a subroutine by other programs and will take the contents of the accumulator and display the corresponding ASCII character on the screen at the current cursor position on being jumped to (JSR) at 0300. Before returning this subroutine will advance the cursor position and if the current line is full it will scroll the screen. Four control codes in the accumulator are intercepted by the program and produce the following action.

0A 	...	Line feed

0C 	...		Form feed i.e. clear screen and home cursor

0D	...		carriage return

7F 	...	back space cursor and delete character

The code 0C must always be used after switch on to initialise the 6845 controller IC, clear the character RAM and home the cursor.

If the SAA5050 characters generated by the codes 0A, 0C, OD and 7F are required on the screen the same characters may be produced using the codes 8A, 8C, 8D and FF which the subroutine does not intercept.

# VDU ACORN 6502 Assembler

0010: 0300 			VDU 	ORG 	$0300

0020: 0300 			SCAP 		“	$0020

0030: 0300 			LINE		“	SCAP 	+01

0040: 0300 			WORK		“	LINE 	+02

0050: 0300 			SCRA		” 	$0400 	memory addresses for the screen

0060: 0300			SCRB 		“	$0500

0070: 0300 			SCRC 		“	$0600

0000: 0300 			SCRD 		“	$0700

0090: 0300 			CRTA 		“	$0800 	6845/6545 crt controller

0100: 0300 			CRT8 		“	$0801

0110: 0300 	A4 	20 	CHATS 	LDY	SCAP 	character to screen

0120: 0302 	C9 	20 		CMPIM 	$20

0130: 0304 	90 	37 		BCC 	CTL 	all control characters

0140: 0306 	C9 	7F 		CMPIM 	$7F

0150: 0308 	F0	27 		BEO 	DELETE

0160: 030A 	20 	CD 03 	TOSCRN 	JSR	 WRCH

0170: 030D 	C8 	INY

0180: 030E 	CO 	28 		CPYIM 	$28

0190: 0310 	90 	05 		BCC 	VDU8 	automatic scroll when line filled

0200: 0312 	20 	80 	03 	FILLED 	JSR 	SCROLL

0210: 0315 	A0 	00 		VDUA 	LDYIM	$00

0220: 0317 	20 	B5 	03 VDUB 	JSR 	CALCN

0230: 031A 	B4 	20 	STY 	SCAP

0240: 031C 	A0	0F 	LDYIM 	$OF 			rewrite cursor position

0250: 031E 	8C 	00 	08 		STY 	CRTA

0260: 0321 	A4 	23 			LDY 	WORK

0270: 0323 	8C 	01 	08 		STY 	CRTB

0280: 0326 	A0	0E 			LDYIM 	$0E

0290: 0328 	8C 	00 	08 		STY 	CRT A

0300: 032B 	A4 	25 			LDY 	WORK 	+02

0310: 032D 	8C 	01 	08 		STY 	CRTB

0320: 0330 	60 			VDUC 	RTS

0330: 0331 	88 			DELETE 	DEY

0340: 0332 	30 	FC 			BMI 	VDUC 	refuse to delete before line start

0350: 0334 	A9 	20 			LDAIM 	‘		write in a blank

0360: 0336 	20 	CD 	03 		JSR 	WRCH

0370: 0339 	A9	7F 			LDAIM 	$7F

03B0: 033B 	D0 	DA 			BNE 	VDUB

0390: 033D 	C9 	0D 		CTL 	CMPIM $0D 	carriage return?

0400: 033F 	F0 	D4 			BEQ 	VDUA

0410: 0341 	C9 	0A 			CMPIM $0A 	line feed?

0420: 0343 	F0	06 			BEQ 	SCROL

0430: 0345 	C9 	0C 			CMPIM $0C 	form feed?

0440: 0347 	F0 	09 			BEQ 	CLEARS

0450: 0349 	D0 	BF 			BNE 	TOSCRN

0460: 034B 	20 	80 	03 	SCROL 	JSR 	SCROLL 	scroll screen and rewrite cursor

0470: 034E 	A4	20 			LDY 	SCAP

0480: 0350 	B0 	C5 			BCS 	VDUB

0490: 0352 	48 			CLEARS 	PHA 			clear entire buffer

0500: 0353 	A0	00 			LDYIM 	$00

0510: 0355 	A9	20 			LDAIM

0520: 0357 	99 	00 	04 	CLEAR 	STAAY SCRA

0530: 035A 	99 	00 	05 		STAAY SCRB

0540: 035D 	99 	00 	06 		STAAY SCRC

0550: 0360 	99 	00 	07 	STAAY 	SCRD

0560: 0363 	C8 				INY

0570: 0364 	D0 	F1 			BNE 	CLEAR

0580: 0366 	84 	20 			STY 	SCAP

0590: 0368	A0	0F 			LDYIM 	$0F

0600: 036A 	8C 	00 	08 	SETCRT 	STY 	CRT A 		set up all the crt parameters

0610: 036D 	B9 	D9 	03 		LDAAY CRTTAB

0620: 0370 	8D 	01 	08 		STA 	CRTB

0630: 0373 	88 				DEY

0640: 0374 	10 	F4 			BPL 	SETCRT

0650: 0376 	A9 	C0 			LDAIM 	$C0

0660: 0318 	85 	21 			STA 	L!NE

0670. 037A 	A9	07 			LDAIM 	$07

0680: 037C 	85 	22 			STA 	LINE 		+01

0690: 037E 	68 				PLA

0700: 037F 	60 				RTS

0710: 0380 	08 			SCROLL 	PHP 				scroll subroutine

0720: 0381 48	 			PHA

0730: 0382 	D8 				CLD

0740: 0383 	A0	28 			LDYIM 	$28

0750: 0385 	20 	B5 	03	 	JSR 	CALCN

0760: 0388 	A5 	23 			LDA 	WORK

0770: 038A 	85 	21 			STA 	LINE

0780: 038C 	A5 	25 			LDA 	WORK 		+02

0790: 038E 	85 	22 			STA 	LINE 		+01

0800: 0390 	A0	0D 			LDYIM 	$0D

0810: 0392 	BC 	00 	08 		STY 	CRTA

0820: 0395 	A5 	21 			LDA 	LINE

0830: 0397 	38 				SEC

0840: 0398 	E9 	C0 			SBCIM 	$C0

0850: 039A 	8D	01 	08 		STA 	CRTB

0860: 039D 	88 				DEY

0870: 039E 	8C 	00 	08 		STY 	CRTA

0880: 03A1 	A5 	25 			LDA 	WORK 		+02

0890: 03A3 	E9 	03 			SBCIM 	$03

0900: 03A5 	8D 	01 	08 		STA 	CRTB

0910: 03A8 	A0	27 			LDYIM 	$27

0920: 03AA 	A9 	20 			LDAIM

0930: 03AC 	20 	CD 	CLEARL 	JSR 	WRCH

0940: 03AF 	88 				DEY

0950: 03B0 	10 	FA 			BPL 	CLEARL

0960: 03B2 	68 				PLA

0970: 03B3 	28 				PLP

0980: 03B4 	60 				RTS

0990: 03B5 	08 			CALCN 	PHP 				do calculation to make sure that the

1000: 03B6 	48 				PHA 				processor and crt controller agree on

1010: 03B7 	D8 				CLD 				position of screen r :

1020: 0388 	18 				CLC

1030: 03B9 	98 				TYA

1040: 03BA 	65 	21 			ADC 	LINE

1050: 03BC 	85 	23 			STA 	WORK

1060: 03BE 	A5 	22 			LDA 	LINE 		+01

1070: 03C0 	69 	00 			ADCIM 	$00

1080: 03C2 	85 	25 			STA 	WORK 		+02

1090: 03C4 	29 	07 			ANDIM 	$07

1100: 03C6 	09 	04 			ORAIM	$04

1110: 03C8 	85 	24 			STA 	WORK 		+01

1120: 03CA 	68 				PLA

1130: 03CB 	28 				PLP

1140: 03CC 60 				RTS

1150: 03CD 	20 	B5 	03 	WRCH 	JSR 	CALCN

1160: 03D0 	84 	25 			STY 	WORK 		+02

1170: 03D2 	A0 	00 			LDYIM 	$00

1180: 03D4 	91 	23 			STAIY 	WORK

1190: 03D6 	A4 	25 			LDY 	WORK 		+02

1200: 03D8 	60 				RTS

1210: 03D9 	3F 			CRTT AB 	= 	$3F 		total number of characters per line ,

1220: 03DA 	28 				= 	$28 		40 characters displayed

1230: 03DB 	33 				= 	$33 		position of horizontal sync

1240: 03DC 05 				= 	$05 		width in (S of horizontal sync pulse

1250: 03DD	1E 				= 	$1E 		total number of character rows

1260: 03DE	02 				= 	$02 		additional no. of lines for 312 total

1270: 03DF 	19 				= 	$19 		25 displayed character rows

1280: 03E0	1B 				= 	$1B 		position of vertical sync pulse

1290. 03E 1 00 				= 	$00 		set non-interlace mode

1300: 03E2 	09 				=	$09 		set 10 lines per character row

1310: 03E3 	68 				= 	$68 		slow blink cursor from line 9

1320: 03E4 	09 				= 	$09 		to line 10

1330: 03E5 	04 				= 	$04 		high address of VDU ram

1340: 03E6 	00 				= 	$00 		low address of VDU ram

1350: 03E7 	07 				= 	$07 		high address of initial cursor position

1360. 03E8 	C0				=	$C0		low address of initial cursor position

Two further programs may be loaded which empty the V.D.U. control subroutine.

Acorn Keywrite .

The keywrite program is entered at MAIN (0280). When this program is first used after switching on a form feed can be sent to the screen to program the 6845 by pressing the 'r' key.

The program then accepts pairs of Hex characters before sending them to the screen, by-passing the control interpreter to allow any code to be sent. The control keys provide the following functions

1 	Line feed 		g 	space

I\ 	delete 			p 	space

V 	carriage return 		s 	space

r 	form feed 		m 	return to monitor

KEYWRT 				ACORN 6502 Assembler

0010: 0280 				KEYWRT 	ORG 	$0280

0020: 0280 				TEMP	* 	$0026

0030: 0280 				RESTRT 	*	$FF04

0040: 0280 				DISPLA 	*	$FE0C

0050: 0280 				VDU 	*	$0300

0060: 0280 	20 	0C 	FE MAIN 	JSR 	DISPLA

0070: 0283 	90 	0E 			BCC 	SEND 		hex key ?

0080: 02B5 	29 	07 		CONTR L 	ANDIM 	$07

0090: 02B7 	F0	18 			BEG 	RETURN

0100: 0289 	AB 				TAY 				look up control keys in table

0110: 028A 	69 	A6 	02 		LDAAY	TA8LE 		-01

0120: 02BD	20 	00 	03	SENDER 	JSR 	VDU

0130: 0290 	4C 	BO 	02 		JMP 	MAIN

0140: 0293 	0A 			SEND 	ASLA

0150: 0294 	0A 				ASLA

0160: 0295 	0A 				ASLA

0170: 0296 	0A 				ASLA

0180: 0297 	85 	26 			STA 	TEMP

0190: 0299 	20 	0C 	FE 	JSR 	DISPLA

0200: 029C 	B0 	E7 			BCS 	CONTRL

0210: 029E 	05 	26 			ORA 	TEMP 		mix in low digit

0220: 02A0 	09 	80 			ORAIM	$80 		fool control character check

0230: 02A2 	30 	E9 			BMI 	SENDER 	forced branch to sender

0240: 02A4 	4C 	0A 	FF RETURN 	JMP 	RESTRT 	M key returns to monitor

0250: 02A7 	20 			TABLE 	= 	$20 		G key gives space bar

0260: 02AB 	20 				= 	$20 		P key gives space bar

0270: 02A9 	20 				= 	$20 		S key gives space bar

0280: 02AA 	0A 				= 	$0A 		L key gives line-feed

0290: 02AB 	0C 				= 	$0C		R key gives form-feed

0300: 02AC 	7F 				= 	$7F 		/ \ key gives delete

0310: 02AD 	0D 				= 	$0D		\ I key gives carriage return

## Acorn Mini-Disassembler

The mini-Disassembler provides a formatted listing of 25 lines of 6502 program instructions in machine code presented in Hexadecimal.

The start address of the program to be disassembled is entered into the m address of the Acorn Monitor using the m key and the dis-assembler program is then executed from 0200 using the g key in the normal way. A formatted 25 lines of instructions will be displayed on the screen and the program ends in a jump back to the monitor. The m address is stepped forwards so re- running the program will display the next 25 program lines.

MINDIS 				ACORN 6502 Assembler

0010: 0200 				MINDIS 	ORG 	$0200

0020: 0200 				MOD	* 	$0000

0030: 0200 				COUNT	*	$000E

0040: 0200 				VDU 	*	$0300

0050: 0200 				RESTRT 	*	$FF04

0060: 0200 	A9 	18 		START 	LDAIM 	$18 		disassemble 251ines

0070: 0202 	85 	0E 			STA 	COUNT

0080: 0204 	D8 				CLD

0090: 0205 	A9 	0C 			LDAIM 	$0C 		start with a form-feed

0100: 0207 	20 	00 	03 		JSR 	VDU

0110: 020A 	A9 	0D 		MAIN 	LDAIM 	$0D 		carriage return/line feed for each line

0120: 020C 	20 	00 	03 		JSR 	VDU

0130: 020F 	A9	0A 			LDAIM 	$0A

0140: 0211 	20 	00 	03 		JSR 	VDU

0150: 0214 	A5 	01 			LDA 	MOD 		+01 display current address

0160: 0216 	20 	58 	02 		JSR 	$PBYTE

0170: 0219 	A5 	00 			LDA 	MOD

0180: 021B 	20 	5F 	02 		JSR 	BYTOUT

0190: 021E 	A0 	00 			LDYIM 	$00

0200: 0220 	A2 	01 			LDXIM 	$01 		x will be the byte count of the opcode

0210: 0222 	B1 	00 			LDAIY 	MOD 		fetch opcode, find it's no. of bytes

0220: 0224 	C9 	20 			CMPIM	$20 		'jsr' is an anomaly and is done first

0230: 0226 	F0 	17 			BEO 	CBYTE

0240: 0228 	29 	9F 			ANDIM 	$9F

0250: 022A 	F0 	15 			BEO 	ABYTE 	binary OXX00000 is 1 byte

0260: 022C 	29 	1D 			ANDIM 	$1D

0270: 022E 	C9 	19 			CMPIM	$19

0280: 0230 	F0	0D 			BEO 	CBYTE 	binary XXX110X1 is 3 bytes

0290: 0232 	29 	0D 			ANDIM 	$0D

0300: 0234 	C9 	08 			CMPIM	$08

0310: 0236 	F0 	09 			BEO 	ABYTE 	binary XXXXXOXO (now) is 1 byte

0320: 0238 	29 	0C 			ANDIM	$0C

0330: 023A 	C9 	0C 			CMPIM	$0C

0340: 023C 	F0 	01 			BEO 	CBYTE 	binary XXXX11 XX is 3 bytes

0350: 023E 	CA 				DEX 				all others are 2 byte

0360: 023F 	E8 				CBYTE	INX

0370: 0240 	E8 					INX

0380: 0241 	A0 	00 		ABYTE 	LDYIM 	$00

0390: 0243 	B1 	00 			LDAIY 	MOD

0400: 0245 	20 	58 	02 		JSR 	SPBYTE

0410: 0238 	E6 	00 			INC 	MOD 		increme

0420: 024A 	D0 	02 			BNE 	NOINC

0430: 024C 	E6 	01 			INC 	MOD +01

0440: 024E 	CA 			NOINC 	DEX 				print all bytes required

0450: 024F	D0	F0 			BNE 	ABYTE

0460: 0251 	C6 	0E 			DEC 	COUNT

0470: 0263 	10 	85 			BPL 	MAIN 		finished the 25 lines

0480: 0256 	4C 	04 	FF	GETOUT 	JMP 	RESTRT

0490: 0258 	48 		SPBYTE 	PHA 				print a space and then the byte

0500: 0259 	A9 	20 			LDAIM

0510: 0258 	20 	00 	03 		JSR 	VDU

0520: 025E 	68 				PLA

0530: 025F 	48 		BYTOUT 	PHA 				print a byte

0540: 0260 	4A 				LSRA

0560: 0261 	4A 				LSRA

0660: 0262 	4A 				LSRA

0570: 0263 	4A 				LSRA

0580: 0264 	20 	68 	02 		JSR 	DIGOUT

0590: 0267 	68 				PLA

0600: 0268 	29 	0F 	DIGOUT 	ANDIM	$0F 		print the bottom Hex digit in A

0610: 026A 	09 	30 			ORAIM	$30

0620: 026C 	C9 	3A 			CMPIM	$3A

0630: 026E 	90 	02 			BCC 	PUT

0640: 0270 	69 	06 			ADCIM	$06

0660: 0272 	4C 	00 	03 	PUT 	JMP 	VDU

The VDU controller may reside in memory with the Keywriter, the Mini-Disassembler or both and subsequently they may be stored on cassette tape in the usual way. User program space is then reduced to the range 0020 through 00FF with the page 0100 to 01FF used for stack space as before. The RAM in the INS 8154 IC's is also free to the user .